## Slide 1: Notes on Usage
See https://github.com/colinoflynn/colins-pcb-intro for latest version of these slides.
See blog post at www.oflynn.com which links to YouTube video presentation(s) of these slides.
My text & photos are CC-SA Licensed – however many images used are not, so if presenting this I leave it up to you to replace them if required.

## Slide 3: WARNING ON THIS LECTURE
This topic needs an entire course, maybe several. I’m giving you one lecture.
Entering Ludacris speed…

## Slide 4: Background to this Lecture
My PCBs:
  ~A few hundred designs over the years
    Many open source, some very basic some more complex
    Some prototype only, some higher volume (>5K)
  2 to 12 layers
  Lots of small parts & high density (BGA).
  I’ve written a few guides over the years on the topic… some of them referenced within here!
Things I haven’t done:
  Heavily cost optimized (e.g., > 10K units or consumer electronics)
  High-frequency RF (> 6 GHz)

## Slide 5: e.g., my PCBs over the years

## Slide 6: PCBs 101

## Slide 7: PCBs 101
https://commons.wikimedia.org/wiki/File:Point_to_point_wiring.jpg, CC SA by Mataresephotos

## Slide 8: PCBs 101: Basic Board
https://www.altium.com/documentation/altium-nexus/understanding-printed-circuit-board-makeup?version=4#single-sided-board

## Slide 9: Old PCBs!
https://www.youtube.com/watch?v=URGfZukAs98

## Slide 10: Milled PCBs

## Slide 11: Another simple milled PCB example:

## Slide 12: Golden Rule of PCB Design
Design your board for how you plan on getting it made and built.

## Slide 13: PCBs 101: PTH (Plated Through Holes)
https://www.altium.com/documentation/altium-nexus/understanding-printed-circuit-board-makeup?version=4#single-sided-board

## Slide 14: PCBs 101 - Basics

## Slide 15: PCBs 101 – Soldermask
Soldermask (Black in this example)
No Soldermask

## Slide 16: PCBs 101 – Silkscreen
Silkscreen (White)

## Slide 17: PCBs 101 - Finish
ENIG
HASL

## Slide 18: PCBs 101 – More Layers

## Slide 19: Multi-Layer Lamination Process
https://morepcb.com/pcb-prepreg/

## Slide 20: Terminology
PCB-A = Printed Circuit Board Assembly
PCB = Printed Circuit Board

## Slide 21: Terminology – Cont’d
Pad
Via
Drill
Trace
Soldermask
Silkscreen

## Slide 22: PCB: Design Software?

## Slide 23: Part 1: PCB Design Basics

## Slide 24: PCB Design Units
Units are normally in mils or mms.
1 mil = 0.001 inch = 0.0254 mm
WARNING: This is unique to PCB design. It’s not a frequently used unit in mechanical design & may be misinterpreted as a something else.
In mechanical design “thou” would be used. Especially outside North America where mm would be more common.

## Slide 25: Trace & Space
https://madpcb.com/glossary/conductor/

## Slide 26: Trace & Space == $$
Trace & Space of 8 mil (0.2mm) or higher can be produced anywhere.
Trace & Space of 6 mil (0.15 mm) is mostly available.
Trace & Space of 5 mil (0.127 mm) is now common on lower-cost boards, but not universal (OSHPark 2-layer PCBs are 6-mil)
Trace & Space of 4 mil is higher-tech.
Accurate as of 2025 – this has been stable for some time, and little indication we are getting towards “normal” 4 mil trace/space usage.

## Slide 27: PCB Trace = Resistance & Inductor

## Slide 28: e.g., comparing two PCB traces passing 2A:
Wider
Narrower

## Slide 29: Circuit Equivalent:

## Slide 32: Good Starting Trace Settings
Trace & Space of 8 mil (0.2mm) or higher can be produced anywhere.
Trace & Space of 6 mil (0.15 mm) is mostly available.
Trace & Space of 5 mil (0.127 mm) is now common on lower-cost boards, but not universal (OSHPark 2-layer PCBs are 6-mil).
NOTE: The lower limit of trace & space won’t be as reliable for a process as going above that limit. Always good practice to keep as large a trace & space as your design allows.

## Slide 33: Trace & Space Defaults
Use 10 mil (0.25mm) trace & space is a good initial setting.
Widen power traces to ~20 mils (~0.5mm) or more.
  You'll see in Group Project 1 how to calculate temperature rise of a trace.
https://www.protoexpress.com/tools/trace-width-and-current-capacity-calculator/

## Slide 34: Via & Drill
You are normally specifying the finished hole size.
PCB manufacturer will take care of selecting a drill to get you the required finished hole size you specify in the design software.

## Slide 35: Annular Ring
https://www.protoexpress.com/blog/dont-let-annular-rings-drive-you-crazy

## Slide 36: Via Tenting
If soldermask covers the vias they are tented.
Note depending on the drill hole sometimes the soldermask doesn’t cover the hole.
Tented Via
(Hole is clear)
Tented Via (hole has slight raise)

## Slide 37: Untented Vias
Untented vias are exposed as here.
Why tent vias?
Reduces risk of shorts or solder bridges.
Looks cleaner.
  NOTE: Silkscreen cannot go over untented vias.
Why untent vias?
Can use vias as test points.
Easier to modify PCB.

## Slide 38: Typical Via Sizes
Good generic one:
20 mill drill (0.5 mm) & 40 mil (1.0 mm) diameter pad
Smallest size for low-cost:
12 mil drill (0.3mm) & 24 mil (0.6 mm) diameter pad
(Now commonly 8 mil (0.2 mm) drill is available)
For higher power increase size & add several in parallel.
NOTE: We commonly call the hole size the “drill”, even though the actual drill size is different. We rarely know the actual “drill”. Just be aware these are different!

## Slide 39: When Designing your PCB:
Check default trace & space settings + via sizes – ensure it matches your process!
  It’s a LOT more work to fix this later.

## Slide 40: Via in Pad

## Slide 41: Via in Pad

## Slide 42: Via in Pad Process
$$$

## Slide 43: Do This NOT That:
Baby Jesus Sad
Baby Jesus Happy*
*Very pedantic people may point out there should be multiple vias to reduce inductance if this is for power

## Slide 44: Route to avoid current loops
https://www.protoexpress.com/blog/best-high-speed-pcb-routing-practices/

## Slide 45: Remember: Your Fields / EM Courses!
https://www.youtube.com/watch?v=nydLMuGB61E&t=13m10s

## Slide 46: EMC Compliance
https://emcfastpass.com/emc-testing-beginners-guide/emissions/

## Slide 47: 2-Layer PCB vs 4-Layer PCB
https://www.youtube.com/watch?v=crs_QLuUTyQ

## Slide 48: Footprints

## Slide 49: Footprints: Standard
Standard footprints designed for production soldering, using solder paste process.
But what if you are doing just a few boards…

## Slide 50: Footprints: Hand Soldering
https://www.davidhaillant.com/smd-soldering/

## Slide 51: SMD vs. Through Hole
Surface mount parts can be more difficult to solder, but once you get used to it you may prefer them!
Lots of automated & semi-automated methods you can use for soldering, a few examples in these slides…

## Slide 52: SMD Footprint Sizes
0805 (Inch) = 2012 (Metric)
Suggest to use 0805 sizes as a minimum to get started.
In industry, most designs are 0603 where space is not a constraint, 0402 is “normal” where some space constraints.
0201 and smaller are used for space constrained.
NOTE: As size goes down power handling capacity, voltage ratings, etc tend to go down. Very little downside to large packages.

## Slide 53: Checking Footprints!
Footprints may have errors. Good practice to always check them against datasheet.
Also good idea to order parts early & test them on a printed copy of the PCB to ensure things “fit” as you expect.

## Slide 54: Soldermask Bridges / Dams
Soldermask between pins (wide pitch part)
Soldermask removed between pads – gap would be too small for soldermask process.

## Slide 55: Planes & Pours

## Slide 56
Let’s assume you’ve got the design already (we’ll see how you can make a design later).
And go onto…

## Slide 57: Part 2: Ordering & Submission

## Slide 58: Manufacturing Process
https://www.protoexpress.com/kb/pcb-manufacturing-overview/

## Slide 59: DRC / DFM Checks
Design Rule Check (DRC) part of Design For Manufacturability (DFM)
DRC is critical.
  Causes delays or broken PCBs.

## Slide 60: File Formats
You are mostly going to deal with “Gerbers” & “NC Drill”.
There are more “recent” file formats that you may come across in industry which have much better control on information.
You may also share a netlist with the fab which is used for electrical test (E-Test).

## Slide 61: Gerber & NC-Drill
https://www.eurocircuits.com/gerber-past-present-and-future/
These file formats are old (1960’s), and have a lot of terminology that reflect how the PCBs were made (see left) using a photoplotter.

## Slide 62: Gerber & NC-Drill
The Gerber files (RS-274-D) contained the traces.
  Encoded as selecting an aperture & moving it around. Still the case.
The NC Drill (NC = Numeric Control) contained the drills for vias & holes.
  Sometimes called Excellon after a brand name.
You may need to specify your file parameters such as:
  Units (mm vs inch)
  “Precision” (how many decimal places are used)

## Slide 63: README File
Very common to include a “README.txt” file which has details:
Board parameters (size)
File information
Contact information (maybe?)
NOTE: Be careful to avoid OVERSPECIFYING things that you are specifying in the ordering process.

## Slide 64: e.g., Minimal README File

## Slide 65: e.g., More detailed README File:
8 Layers
Physical stackup details
E-Test Requirement
Design Technology

## Slide 66: Sidenote: Inverted Layers?
Via connected to the plane
Hole isolated from the plane
The green here marks where there isn’t copper on this layer (inverted).
Plane layers are often inverted since they are mostly copper. This helps visualize them and keep file sizes lower.
Normally the fabs will pick up on this, but good to specify.

## Slide 67: Manufacturing Drawing
Various details of the board manufacturing requirements.

## Slide 68: PCB Fabs of Interest
(China) JLCPCB: Currently most popular overseas fab
(China) PCBWay: Access to higher-end processes than JLCPCB, more expensive/less user friendly.
  WARNING: Chinese New Year / Spring Festival happens shortly, PCB fabs shut down…
(EU) EuroCircuits: Good website, good prices & speed
(USA) OSHPark: Slower due to shipping here, but great service & very “maker-friendly”.

## Slide 69: Quoting via JLCPCB
Outline should be autodetected.
Layers should be autodetected.
1.6mm (0.062”) is normal thickness.
Select Lead-Free or ENIG
Green may be fastest…
Get more than 5 if all group members get one & to have lots of spare for soldering.
Upload a .zip file

## Slide 70: README File for Generic Ordering
If I plan on selecting soldermask via JLCPCB interface, don’t specify one here! Chance I forget to update the file which may cause them to hold the job while they confirm what I actually want.

## Slide 71: Ordering Full Assemblies
JLPCB can be used for even ordering simple pre-built boards like the one to the left.

## Slide 72: Bill of Material (BOM)
BOM is a critical file that contains your parts.
You can maintain this separately OR export it from your design files (preferred).
For JLCPCB they have a special format they want! But generally may look like this:

## Slide 73: Pick-n-Place Machine

## Slide 74: e.g., Full Production Line
https://www.youtube.com/watch?v=9uet6TNtUXI

## Slide 75: PNP / CPL File Format
Manufactures may need specific format – see documentation for your software.

## Slide 76: Tape & Reel
https://www.reelservice.com/blog/2018/09/18/the-a-z-glossary-of-tape-reel-part-1-a-h/
https://electronics.stackexchange.com/questions/694163/smd-resistor-rotation-on-tape-and-reel

## Slide 77: PNP Gotchas
The rotation of the parts needs to be relative to the part position in the “tape”.
This is especially important with diodes (LEDs) where it won’t be obvious if the part is backwards.
  You will often supply documentation to confirm the anode or cathode of each diode.
Some workflows let you do this automatically (JLCPCB, MacroFab, etc).
  Always check – it may have something simple like a “pin 1” indicator for LEDs, go check if Pin 1 means anode or cathode & that your files agree!!

## Slide 78: JLCPCB Assembly Service
https://cart.jlcpcb.com/quote?fromDemo=yes

## Slide 79: JLCPCB Parts (LCSC)
Use special suppliers where possible with JLCPCB – many parts are not available in each others markets.

## Slide 80: Finding Replacement Parts
NOTE: The search isn’t that good. Here I tried a few variations (560 resistor, 560 ohm resistor, 560R resistor).
Check carefully on hover-over that it looks reasonable & package size is what I need (0402), then click the item to see all details.

## Slide 81
E.g., here “560 0402” is coming up with 5.6K, 56R, 56k, etc

## Slide 82: SIDEBAR: Suffixes as Multipliers
Very common to use R as “ohms”, then drop it for higher values. The suffix also becomes the decimal place:
  560R = 560Ω
  560k = 560kΩ
  5k6 = 5.6kΩ
For capacitors, common to use n or u:
  100n = 100nF
  2u2 = 2.2µF

## Slide 83: Placement Preview

## Slide 84: Fixing Orientation
See https://jlcpcb.com/help/article/pcb-assembly-faqs-part-2 if using this service.
They rely on silkscreen markings to confirm polarity/rotation.
The previewer may be wrong, this will get fixed later and you will need to confirm it.

## Slide 85: Sidebar: Pin 1, Anodes/Cathode Markings
Pin 1 marking is visible with part mounted.

## Slide 86: Sidebar: Pin 1, Anodes/Cathode Markings
What does this polygon mean?
Be sure to document if anode or cathode!!

## Slide 87: Sidebar on Sidebar: IC Ejection Marks
Pin 1 Marking
NOT pin markings.
These are from moulding process.

## Slide 88: Sidebar on Sidebar: IC Ejection Marks
Pin 1 Marking
NOT pin 1.
Ejector marks are much shallower. Look carefully!

## Slide 89: Part 3: KiCAD Introduction

## Slide 90: Getting / Installing KiCad
https://www.kicad.org/download/

## Slide 91: Starting a Simple Project

## Slide 92: First Time: Defaults should be OK!

## Slide 93: Project: Keep It Simple!
Make a simple first project (See Group Assignment).
Keep a single sheet to avoid learning about hierarchy for now.

## Slide 94: Symbols & Footprints
Symbol libraries hold the symbols used on the schematic.
Similar libraries hold the footprints we’ll use to design the PCB.

## Slide 95: Schematic Entry

## Slide 96: Schematic Entry
Search for “Capacitor”
Click on the Symbol
This is a generic symbol with no footprint. We’ll need to specify one!

## Slide 97: Schematic Entry

## Slide 98: HINT: Selecting Parts
If selecting parts (like op-amps, microcontrollers, etc) try to stick with parts that are in the library, saves you from making footprints.
Decide on what you are comfortable soldering. If DIY stick with through hole or large SMD. If using JLCPCB Assembly stick with SMD (they prefer SMD to through hole).

## Slide 99: Adding Power
The same name gets connected together, actual name doesn’t matter.
But make sure you use the same name for e.g., all your 3.3V nets!

## Slide 100: Assigning Footprints
Double-click…
Click…

## Slide 101: Assigning Footprints

## Slide 102: Assigning Footprints
WARNING: You can assign incompatible footprints. Check carefully what anode/cathode marks to with diodes, and parts like transistors that may have different pinouts available.

## Slide 103: Assigning Part Numbers?
I can add other fields to specify specific part numbers.
Assign value here

## Slide 104: Hint: Adjusting your Default Template
Set up some defaults if you want them to always be on your symbols!
Saves you from remembering all the fields…

## Slide 105: Finding Parts on Digikey / Mouser

## Slide 106: Typical Resistor Search
<Live Demo, backup slides >

## Slide 108
Filter by highly available and/or lower price. Good enough!

## Slide 109: Resistor Quick Ref
Check power handling capacity. If powering bright/large LEDs do calculation of power loss in resistor, keep that at < 50% of rated.
  Watch for heating effects – through hole resistors may be preferred here!
1% & 5% resistors are the same price with smaller resistors. Tend to just order 1%...
Don’t get too caught up on anything else for now.

## Slide 110: Typical Capacitor Search

## Slide 111: Capacitor Biasing Effect

## Slide 112
Temperature Coefficient

## Slide 113: Capacitor Quick-Ref
Stick to ceramic caps unless you need higher values for e.g., filtering of input power.
  WARNING: Some types, such as tantalum, are very sensitive to reverse polarity and over-voltage.
  Don’t rate only based on expected voltage! Consider biasing for ceramic caps.
  BUT: If you set the voltage TOO high you will pay $$$ or need too large a package.
Capacitor tolerance is looser: ±10% is a good value.
  For higher values larger tolerance swings are reasonable.
X7R/X5R is a good temp coefficient to start with, but often not too important.
For sensitive values (such as crystal capacitors) C0G or NP0 are more stable.

## Slide 114: Typical LED Search
LED characteristics can vary a lot – maybe you don’t want SMD? Do you want a super-bright LED?

## Slide 115: Finding Connectors
Connectors can be tricky to search for. Let’s say I want some standard terminal headers:

## Slide 116: Finding Connectors
Always check “In Stock” first!

## Slide 117: Visual Clues
Look at photos – for example if I want normal unshrouded connectors, I can see this one is right:
I know to search “Unshrouded” now…

## Slide 118: Visual Clues
I can now select “Unshrouded” and hit “Apply All” to filter results again.

## Slide 119: Selecting Parts
Selecting parts requires careful consideration of everything we need.
Can be overwhelming at first! Take some time to look through. Use existing designs if you can find them as reference too.
Let’s assume we finished that…

## Slide 120: Syncing to PCB
Hit this…
Read warnings or errors – might happen if you have the wrong footprint!
Hit this now.

## Slide 121: Placing Parts
Click & drag parts (watch you get the part and not the text).
Hit ‘r’ to rotate while holding down button.
Ratsnest

## Slide 122: Placing Effort
Time spent improving placement will make your routing much easier.
This can take some time to develop, since you need some experience routing to understand what makes sense.

## Slide 123: Setting up Widths

## Slide 124: Routing
Press “x” to start routing. Click on a point and you see the ratsnest follow you:
Press w key to switch between defined trace widths (Shift-W goes backwards).

## Slide 125: Online DRC
Online Design Rule Check enabled by default.
Prevents you from doing illegal things like routing trace too close for your design rules.
In this example I cannot drag it through here.

## Slide 126: Switching Sides (Via)
Press ‘v’ button to place via. Switches sides automatically!

## Slide 127: Autorouter??
Autorouter sounds like it could be magic!
Despite many peoples negativity they can work, but they require a lot of effort defining what you want them to do. In many circumstances not worthwhile.
  E.g., you inherently know which traces are high current or sensitive. AutoRouter has no idea, you need to make a class, define the trace widths, etc.
I’ve used them on some boards for tests, rarely pleased with results.

## Slide 128: Check Mechanical Size & Add Mounting Holes
Think about how you will mount this:
  If fitting in breadboard, mount headers on 0.1” grid space
  If bolting to something, make a convenient mounting hole
HINT: Add a “Mounting Hole” part on schematic and assign it a “Mounting Hole” footprint.
This will ensure it stays around and isn’t forgotten!
For mechanical strength some hole patterns have additional small vias within them.

## Slide 129: Pretty Up Silkscreen

## Slide 130: Pretty Up Silkscreen
Move the reference designators so it doesn’t overlap the other component pads.
Values are for our ref & won’t get printed on silkscreen. We can turn this layer off if it starts to look too messy.

## Slide 131: Pretty Up Silkscreen
Press Alt-3 (or view 3D viewer) to check what it will look like.

## Slide 132: Add Outline
Add a closed outline on the EdgeCuts layer

## Slide 133: Ground Pours
Consider adding ground pours.
Make sure you have some vias to GND they will connect to!
…we’re going beyond the time limit here, see many of the other great tutorials…

## Slide 134: DRC Checks

## Slide 135: Exporting Files

## Slide 136: Exporting Files
1. Put a folder here such as “gerber_outputs”
This will keep all your files together so you don’t miss one!
2. Then press this button.
3. Then press this button.

## Slide 137: Exporting Files Cont’d
This should have been populated automatically. Same as gerbers!
2. Then press this button.
3. Then close everything.

## Slide 138: Zipping Together
Zip all the files.
Sanity check the dates/times are within a few mins of each other.
(In case a file didn’t export)

## Slide 139: Testing
Drag your file here
Check the preview! Should match what you expect.
(Example error: I didn’t include a board outline in kicad so this is cut too close!)

## Slide 140: Part 4: Prototype Bring-Up

## Slide 141: Soldering 101
Hopefully you have previous soldering experience!
Modify your design based on your team(s) experience, OR plan on ordering preassembled boards.

## Slide 142: SMD Soldering Guides
Surface mount soldering is often done with solder paste.
Can also do it with regular solder – use lots of flux if so!

## Slide 143: Hand Soldering & Low-Cost
I've got a guide from 2003:
https://colinoflynn.com/wp-content/uploads/2025/01/smd_soldering.pdf

## Slide 144: Solder Paste
Solder spheres & flux mixed together.
Often needs to be stored at low temp or the flux becomes too liquid & separates!
Available in tubes (left) and tubs.

## Slide 145: Solder Paste Usage
Best usage with a stencil (can order with PCB).
But can also use a toothpick to “paint” on pads. If you are careful this will work with multi-package SMD well!
See the next three videos…

## Slide 146: e.g., Hand Assembly Example
https://www.youtube.com/watch?v=-DMYJmB4naA
https://colinoflynn.com/2015/10/low-cost-smd-soldering-setup/

## Slide 147: e.g., Hand Assembly Example screenshot
https://www.youtube.com/watch?v=-DMYJmB4naA

## Slide 148: Soldering with a Skillet
https://www.youtube.com/watch?v=i8zzNZV8AlU&t=2s

## Slide 149: REMEMBER THE GOLDEN RULE
Design your board for how you plan on getting it made and built.
If you might use skillet assembly, keep all SMD parts on top side only!

## Slide 150: Bring-Up Best Practices
If assembling your own board:
  Assembly a smaller portion and test at a time.
  E.g., I may build up the power supply section of a board first
Use current limited power supplies if possible (if board doesn’t need max current initially).
Confirm as much as you can is working before doing “dangerous” things (like triggering a high-current mode).

## Slide 151: Thermal Camera Checks
Use of a thermal camera can be helpful on important bring ups to watch for “hot spots” before you feel (or smell) them:

## Slide 152: Bodging & Repairs
You may need to modify the PCB to fix things! Typical operations:
1. Cut a trace – easy to use a small drill bit for this (handheld):

## Slide 153: Bodging & Repairs
2. Solder a bodge wire to fix a missing connection. Often used in combination with the drilling to re-route.
Or to repair (as in right)
https://personal.garrettfuller.org/

## Slide 154: Further Learnings
That’s it! There is tons (and tons) of information out there:
Reference books
YouTube (EEVBlog has a lot of videos on these topics)
Forums
Don’t get overwhelmed – make mistakes. Ignore some of the online overly pedantic advice. Have fun!